# AGGRESSER Ride Plate

This ride plate is designed to bolt to your bottom nozzle bolts. When bolted to the nozzle the plate should sit on top of the stock plate. This allows for the front end of the ski to come up when accelerating for top speed. It also allows for a more controllable ride at high speed. By having the step in the two plates, you are having the benefit of an extended plate with out losing speed.

Take a straight edge to the stock ride plate and hull (front of plate). If the ride plate drops below the hull, you must file that edge down so it is flush (tucked up) with the hull. Always check the plate before riding for tightness

ZXI 98-03 you must cut the back of stock plate so it is flush with the hull.

# AGGRESSER ride plate

This ride plate is designed to bolt to your bottom nozzle bolts. When bolted to the nozzle the plate should sit on top of the stock plate. This allows for the front end of the ski to come up when accelerating for top speed. It also allows for a more controllable ride at high speed. By having the step in the two plates, you are having the benefit of an extended plate with out losing speed.

take a straight edge to the stock ride plate and hull (front of plate). If the ride plate drops below the hull, you must file that edge down so it is flush (tucked up) with the hull. check the plate before riding for tightness

ZXI 98-03 you must cut the back of stock plate so it is flush with the hull.