# AGGRESSER SPONSONS

Congratulations you have just purchased the best sponsons on the market. These sponsons have been thoroughly tested and designed to give you flawless results. When installed properly you will notice a dramatic increase in overall handling and performance.

Installation: Read completely before installing!

- Remove original sponsons from boat and clean surface of dirt & silicone. rinse new sponson with water let dry (to get the resin dust off).

- Apply Thick beads of RTV SILICONE over the hull and holes where sponson will be placed and all over back side of sponson that makes contact to hull. (silicone should gush out sides when installed) Also put silicone on the bolts. We will not warranty sponsons that break due to lack of silicone or tightness!!!!(Black RTV silicone is the strongest)

- Place the sponson against the hull.

- Using the back 3 holes except for Sea Doo (Highest hole is most aggressive).

- Add your nuts & bolts and tighten . Wipe off excess silicone and let dry 24 hrs.  Add a bolt, washer’s and nut with silicone to plug open Unused hole. Seadoo’s use your oem washer’s on the inside of hull with the Backing plates supplied (excludes RX,RXX).

- Always check over the sponsons, scoop grate, nozzels and rideplate to make sure everything is secure each time before riding.

- Make sure you have no silicone on bottom of hull, scoop or ride plate!

NOTE:

Sea Doo RX: Use the locking nuts over the stock backing bracket. The stock threads are not strong enough. Rear Aggressor sponson hole goes to 2nd hole from the back of hull. Use the extra bolts to fill in open holes.

Sea Doo Pre 1991. Put fin up to side of hull 3inches from rear and let fin hang down 1.5 inches. Mark the three top holes and drill. Put backing plates on inside of hull.

STXR: Remove stock sponsons then plastic strip. Add Aggresser to last three holes directly against hull. Use lots of silicone! Plug remaining holes with silicone or screws.

Sea Doo all except RX: use our Hull Reinforcement plates inside of hull.

WaveRaider: Use your stock studs Install sponson then cut off the excess length of stud with hack saw. File down rough edges. Do not forget silicone.

GP1200R/1300R: Remove stock sponsons, Remove 10mm head bolts (you will not use those bolts or holes anymore) Remove 6mm hex bolts and add Lots of silicone to angled spacer plate BOTH sides and back side of sponson fin, Add our 6mm bolts into fin, plate then hull and tighten. Wipe off excess silicone.

NOTE:

Do not bend or force sponson to fit if holes do not line up.

Do not let your boat rock on beach.

Do not use silicone on bottom of hull or on rideplate!!!

Warning: These sponsons Are very aggressive. Take time to get use to them. On high speed turns they (boats) can throw you off if you are not ready, so hold on tight. Also tell every rider who will ride your boat the same.  909-899-7070

GP1200/800/760 instructions: remove stock sponsons

1, Set sponson to side of hull line up with rear hole. let it hang 1.5 inches down.

2, Mark the top three holes and drill (Makes sure you will be able to reach holes from inside of hull).

3,Add silicone heavily to back of sponsons.

4 Put bolt through washer, then sponsons then in the holes that where drilled.

5 add silicone to the back plate and put inside of hull over the bolts.

6 add washer then nuts and tighten.

7, Add screws and tighten. Wipe off excess silicon and let dry 24hr.

# Text boxes

Rancho Cucamonga, CA

PH 909-899-7070   WWW.AGGRESSER.COM