# INSTRUCTIONS

Congratulations, you have just purchased the best Exhaust system on the market. These systems have been thoroughly tested and designed to give you flawless results. When installed properly you will notice a dramatic increase in overall performance.

Remove original system.

Recommended corrected compresion150psi head.

- Install new manifold and torque 20 ft lbs. (900 ZXI only)

- Put coupler on head pipe, then connect chamber. Making sure they are snuggled together for a perfect fit. (outside of boat)

- Add clamps to outer edges of coupler. Be sure to have the nut where you can tighten or loosen clamp when system is in boat.

- Loosen gas tank and slide forward.

- Look at head pipe flange (note the ¼ cooling hole) and set gasket on flange making sure all holes line up (Including cooling hole in gasket).

- Install system over motor toward gas tank and into place.

- Loosen coupler clamps and adjust system to align for head pipe bolts then install. (Make sure chamber is not hitting on hull or motor mounts)

- Tighten clamps (outer edge).

- Install hoses as in diagram and add bypass where you feel it is out of way.

- Take the ½ inch 90* brass fitting out of the old exhaust system and replace the brass fitting in head.

- Take the ½ inch water exit hose and run it to the top of head.

- Ride for 5 minutes and check coupler clamps and bolts.

NOTE: 1996/97 Carb settings lower pop off to 22 lbs. Hi speed ¾, low speed ¾.Then it is strongly recommended that you lake tune or tank tune. If RPM is over 7500, go up in prop to bring RPM down and increase top speed.1998-02 cv carb specs, There are 3 different ways  to re-jet: 1st Add shim to needle and cut 1mm off needle-retaining cap and add 40 pilot (.40mm) and leave the stock 165main. Then adjust bottom end screw. The 2nd way: drill main jet to 1.70mm, pilot .40mm and adjust pilot screw 2 turns.  By adding or removing shims from the needle you can fine tune your carb. 3rd way is to add 2 shims and leave the jetting stock. You must have a qualified tech tune your ski so as to not run to lean. The shims affect the midrange to top end. When adding shims trim 1mm off the needle-retaining cap on the unthreaded area before threads per shim. Do not lose the spring!!

If you have any questions, please call  (909) 899-7070.

NOTE: Chamber should not over heat! Or change colors. If it does, stop engine immediately and go over cooling system. Make sure hoses and gaskets are clear from blockage and leaks. We will not warranty over heated chambers.

Note, over heating problems and solutions.

Check hoses and fittings for partial blockages.

Check hose from pump to hull for too much bend reducing inner diameter and volume.

Make sure there are no leaks; leaks reduce pressure in the water system.

Cavitations also reduce pump pressure, so make sure you have a prop in good condition.

Make sure head pipe gasket is aligned

On second brass fitting from front of head pipe there is a.090 hole underneath. Check for blockages. This hole allows water into chamber.

In addition, it has been known for the baffles in the water box to brake and come lose and Plugging up the exhaust exit hole on the water box. This will cause increased backpressure and overheating resulting in chamber popping off.

If you would like 50 additional RPM, Take a long ¼ drill bit and drill out 5+holes in the water box 1st baffle. This will let the water box flow better. And, increase’s top end.